## Slide 1: Lecture - 04

## Slide 2: CPU Organization
The primary function of the CPU is to execute sequences of instructions, which are stored in memory.
The execution is carried out in three steps:
The CPU transfer instruction and when necessary, their input data (operand) from main memory to registers in the CPU.
The CPU executes the instruction in their stored sequence except when the execution sequence is explicitly altered by a branch instruction.
When necessary, the CPU transfers data (results) from the CPU registers to main memory.

## Slide 3: External Communication
CPU
Main Memory MM
Instruction
Data
Processor-memory communication without a cache
CPU
Cache Memory CM
Main Memory MM
Instruction
Data
Data
Instruction
Processor-memory communication with a cache

## Slide 4: External Communication
CPU can perform a memory load or store operation from cache in a single clock cycle. On the other hand, the same operations take many clock cycles if they are performed from main memory.
CPU considers the cache and the main memory as a single, seamless memory space consisting of 2m addressable storage locations M(0), M(1), …. M(2m-1).

## Slide 5: Communication with IO Devices
CPU communicates with IO devices in much the same way as it communicates with external memory.
The IO devices are associated with addressable registers called IO ports to which the CPU can store a word or from which it can load a word.

## Slide 6: Communication with IO Devices
In some computers, memory locations and IO ports share the same set of addresses, so an address bit pattern that is assigned to memory cannot also be assigned to an IO port, and vice versa. This approach is called memory–mapped IO.
Some computers employ IO instructions that are distinct from memory-referencing instructions. These instructions produce control signals to which IO ports, but not memory locations, respond. This approach is called IO-mapped IO.

## Slide 7: User and Supervisor Programs
A user or application program handles a specific applications.
A Supervisor programs manages various routine aspects of the computer system. It is typically part of the computer’s operating system.

## Slide 8: User and Supervisor Programs
For normal operation, CPU continuously switches back and forth between user and supervisor programs.
The requests for supervisor services from the secondary memory and IO devices are known as interrupt.
In the event of interrupt, the CPU suspends execution of the current program and transfer to an appropriate interrupt handling program.
CPU frequently check for the presence of interrupt request.

## Slide 9: CPU Operation
Begin
Fetch the next instruction
Execute the instruction
Are there interrupts waiting?
Transfer to interrupt handling program
No
Are there instruction waiting?
Yes
Yes
No

## Slide 10: CPU Operation
The sequence of operations performed by the CPU in processing an instruction constitutes an instruction cycle.
Processing of all instruction generally requires two steps:
Fetch step - a new instruction is read from the external memory.
Execute step - The operations specified by the instruction are executed.

## Slide 11: CPU Operation
The actions of the CPU during an instruction cycle are defined by a sequence of micro operations, each of which involves a register transfer operation.
The time required for the shortest well-defined CPU micro operation is the CPU cycle time or clock period Tclock.
The number of CPU cycles required to process an instruction varies with the instruction type.

## Slide 12: Accumulator-based CPU
System Bus
Instruction
Decoder
IR
AR
PC
DR
AC
Arithmetic-Logic Unit
To M and IO devices
PCU
DPU
PCU = Program Control Unit
AR = Address Register
(Stores the address in memory where the CPU wants to read/write data)
IR = Instruction Register
(Holds the current instruction being decoded/executed)
PC = Program Counter
(Stores the address of the next instruction to be executed)
DPU = Data Processing Unit
AC = Accumulator Register
(Holds intermediate arithmetic and logic results)
DR = Data Register
(Temporarily holds the data read from or written to memory)
Control Signal

## Slide 13: Accumulator-based CPU
Accumulator-based architecture always stores the intermediate results of calculations in a special register, which is the accumulator. An accumulator machine is known as a 1-operand machine.
An instruction that refers to a data word in M contains two parts, an opcode op and a memory address adr and I = op.adr
Each instruction cycle begins with the instruction fetch operation IR.AR = M (PC), where IR=op and AR=adr. Here PC contains the address of the current instruction in the memory.

## Slide 14: Accumulator-based CPU
Instruction that do not reference M do not use AR. Their opcode part specifies the CPU registers to use, as well as the operation to be carried out.
Once it has placed the opcode of I in IR, the CPU proceeds to decode and execute it. At this point, the CPU can increment PC in order to obtain the address of the next instruction.

## Slide 15: Load and Store Operation
The load instruction transfers a word from the memory location with address adr to the accumulator.
AC := M (adr)
The store instruction transfers a word from AC to M. M (adr) : = AC

## Slide 16: Programming Consideration
Data processing operations normally requires up to 3 operands. For example, Z:= X + Y.
The accumulator based CPU supports only single-address instructions.
A program that implement Z:=X+Y, where X, Y and Z all refer to data words in M, can take the following form:

## Slide 17: Programming Consideration
HDL format Assembly language format Comment
AC:=M(X) LD X Load X from M into AC DR:=AC MOV DR, AC Move contents of AC to DR AC:=M(Y) LD Y Load Y into AC AC:=AC+DR ADD Add DR to AC M(Z):=AC ST Z Store contents of AC in M
HDL = Hardware Description Language
VHDL = VHSIC HDL (VHSIC = Very High-Speed Integrated Circuits)

## Slide 18: Programming Consideration
Consider an instruction of form: AC:= fi (AC, M ( adr)) which require to move M(adr) to or from DR and one to perform the operation fi.
Memory reference complicates the instruction-decoding logic.
Overall execution time should be reduced.

## Slide 19: Programming Consideration
HDL format Assembly language format Comment
AC:=M(X) LD X Load X from M to AC AC:=AC+M(Y) ADD Y Load Y into DR and add to AC M(Z):=AC ST Z Store contents of AC in M

## Slide 20: Instruction Set
The instruction set of the accumulator based CPU:
Type Instruction HDL format Assembly format
Data Load AC:=M(X) LD X Transfer Store M(X):= AC ST X Move Register DR:=AC MOV DR, AC
Data Add AC:=AC+DR ADD Processing Subtract AC:=AC-DR SUB And AC:=AC and DR AND Not AC:= not AC NOT
Program Branch PC:=M (adr) BRA adr Control Branch zero if AC = 0 then BZ adr PC:=M (adr)

## Slide 21: Instruction Set
The arithmetic operation negation:
HDL format Assembly language format Comment
DR:=AC MOV DR, AC Copy contents X of AC to DR AC:=AC-DR SUB Compute AC = X – X = 0 AC:=AC-DR SUB Compute AC = 0 – X = -X

## Slide 22: A Multiplication Program
Consider The program should implement AC:=AC×N where, the multiplicand is the initial content of AC and the multiplier N is a variable stored in memory.
AC×N is implemented by executing the ADD instructions N times in the form AC+AC+………..+AC
The memory location storing N acts as a count register and after each add operation, it is decremented by 1 until it reaches 0.
The test for N=0 is performed by means of BZ instruction.
The memory locations: one – stores constant 1 mult– store N
ac – store Y
prod– partial product

## Slide 23: A Multiplication Program
Line Location Instruction/ Data Assembly format |  |  | 
0 | one | 00…………..01 | 
1 | mult | N | 
2 | ac | 00………….00 | 
3 | prod | 00………….00 | 
4 |  | ST ac | 
5 | Loop | LD mult | AC:= M (mult)
6 |  | BZ exit | If AC= 0 then exit
7 |  | LD one | AC:= M ( one)
8 |  | MOV DR, AC | DR:=AC
9 |  | LD mult | AC:= M (mult)
10 |  | SUB | AC:=AC-DR
11 |  | ST mult | M (mult):= AC
12 |  | LD ac | AC:= M (ac)
13 |  | MOV DR, AC | DR:=AC
14 |  | LD prod | AC:= M ( prod)
15 |  | ADD | AC:=AC+DR
16 |  | ST prod | M ( prod): =AC
17 |  | BRA Loop | 
18 | exit |  | 

## Slide 24: Several Limitations of Accumulator-based CPU
Because of few data registers in CPU, a considerable amount of time is spent shuttling the same information back and forth between the CPU and memory.
It would both shorten the program and speed up its execution if it is possible to store the quantities 1, N, Y and P in their own CPU registers, as they are repeatedly required by the CPU.