## Slide 1: Lecture - 06

## Slide 2: Classifying Instruction Set
CISC = Complex Instruction Set Computer
  Large number of instruction format in instruction set architecture (ISA)
  Large number of addressing schemes and instruction types
  Varying size of instructions
  Multiple cycle instruction execution
RISC = Reduced Instruction Set Computer
  Small number of fast instruction format
  Fixed instruction format, fixed length
  Fast and single cycle instruction execution
  Large number of general purpose registers
  Typical for load/store architectures

## Slide 3: RISC Vs CISC
CISC (complex instruction set computer)
  VAX, Intel X86, Motorolla 680X0, etc
RISC (reduced instruction set computer)
  MIPS, DEC Alpha, SUN Sparc, IBM 801,ARM6, etc

## Slide 4: RISC Vs CISC
CISC | RISC
Variable length instruction | Single word instruction
Large number of format | Small number of format
Memory operands | Load/store architecture
Complex operations | Simple operations

## Slide 5: Instruction Format
An instruction specifies
the operation to be carried out by the processor.
the set of operands to be used in the operation. It includes both the input data of the operation and the result that are produced.
In assembly language notation, an instruction format can be written as
op X1, X2, ….., Xn
opcode
Addresses= register / memory

## Slide 6: Instruction Format for RISC1
As memory addressing is restricted to load and store instructions, so the operands of most instructions are register addresses, Which are short and easy to accommodate in a one-word format.
Set condition code Set immediate address
The register-to-register operation form
Rd:=F(Rs, S2)
Rd – Destination register, Rs – First source register, S2 – Second source register
If bit 13 = 1, then S2 is interpreted as an immediate address
Opcode |  | Source Rs | Destination Rd |  | Source S2
31
23
18
12
0

## Slide 7: Operand Extension
A CPU is designed to process data words and addresses of one specific length.
Instruction contains operands fields that are shorter than standard word size.
This problem is unavoidable in RISC instructions.
Two methods to extend short operand values to full- size, signed or unsigned numbers:
  Sign Extension
  Zero Extension

## Slide 8: Sign Extension
Suppose a short m-bit, twos-complement number N is used in an n-bit arithmetic operation. This technique replicates the leftmost bit s of the short operand N, which corresponds to its sign bit, n-m times.
Example: N = 10101 01010101
NSign-extended= 11111111111111111111010101010101
n-m = 19 13

## Slide 9: Sign Extension
N = 10101 01010101= -264610
It maintains a number’s correct sign and magnitude.

## Slide 10: Zero Extension
If N is an unsigned binary number, then it is always extended by leading 0s, independent of the value of s.
Example: N = 10101 01010101
Nzero-extened = 00000000000000000001010101010101
n-m = 19 13

## Slide 11: Address Extension
Suppose memory address is n-bit, we have to construct it from a short m-bit address field, where n > m.
Zero extension does not allow m-bit address to refer to all 2n possible addresses.
The solution used is to treat the short memory address as a modifier. It is added (in zero-extended form) to a full length memory address stored in a CPU register, known as base register.
This solution is used in both CISC and RISC processor.

## Slide 12: Address Extension
Example: STB Rs, Rd(S2) is equivalent to M(Rd+S2) := Rs[24:31]
The memory address Rd+S2 is called effective address.

## Slide 13: Addressing Modes
The purpose of the address field is to point to the current value V(X) of some operand X used by the instruction. The way of specifying this value is called addressing mode.
The addressing mode of X affects the following issues:
  The speed with which V(X) can be accessed by the CPU.
  The ease with which V(X) can be specified and altered.
Addressing mode:
  Immediate Addressing
  Direct Addressing
  Indirect Addressing

## Slide 14: Immediate Addressing
The value V(X) of the operand X is contained in the address field itself.
X is called immediate operand.
X is constant because it is undesirable to modify instruction fields during execution.
Example: A:=99
  In Intel 8085 series it is MVI A, 99
  In Motorola 690X0 series it is MOVE #99, D1 (D1=A)

## Slide 15: Direct Addressing
The address field in the instruction specifies the storage location that contains V(X).
The storage location can be memory address or register.
V(X) can be varied without modifying the instruction address field.
Example:
A:=B
  In Intel 8085 series it is MOV A, B
  In Motorola 690X0 series it is MOVE D2, D1 (D1=A, D2=B)

## Slide 16: Indirect Addressing
The instruction contains the address W of a storage location, which in turn contains the address X of the desired operand value V(X).
By changing the content of W, the address of X can be changed without modifying the instruction address field.

## Slide 17: The Three Addressing Modes
LOADI | 99 | 
AC
Immediate Addressing
LOAD
X
99
W
X
AC
Direct Addressing
LOADN
W
X
99
W
X
AC
Indirect Addressing

## Slide 18: Relative Addressing
Direct addressing requires the complete operand address to appear in the instruction operand field. This address is used without modification. Generally, only partial addressing information is included in the instruction and the CPU must construct the complete (absolute) address.
Relative addressing is an address construction technique.

## Slide 19: Relative Addressing
In relative addressing, the operand field contains a relative address, called offset/displacement D. The instruction also implicitly or explicitly identifies other storage locations R1, R2,….,Rk (usually CPU registers) containing additional addressing information. The effective address A of an operand is computed by the function f(D, R1, R2,….,Rk). In most cases, A:=R+D.

## Slide 20: Advantages of Relative Addressing
Since all the address information is not included in the instructions, instruction length is reduced.
By changing the contents of R, the processor can change the absolute addresses referred to by a block of instructions B. It allows the processor to move the entire block B from one region of main memory to another without changing the contents of the instructions of B. Here, R is referred to as a base register and its contents as a base address.

## Slide 21: Advantages of Relative Addressing
R can be used for storing indexes to facilitate the processing of indexed data. Here, R is called index register. The instruction address field D contains the address of the first item X(0) and R contains the index i. The address of item X(i) is D+R. By changing the content of R, a single instruction can be used to access any item X(i) in the given data list.

## Slide 22: Drawbacks of Relative Addressing
Relative addressing requires extra logic circuits and processing time needed to compute addresses.

## Slide 23: Auto Indexing
Indexed items are frequently accessed sequentially. So an access to X(k) stored in memory location A is immediately followed by a reference to X(k+1) or X(k-1) stored in location A+1 or A-1, respectively. So, addressing mode that automatically increment or decrement an address can be defined, which is known as auto indexing.
Example: -(A3) [Motorola 680X0 series] indicate that the content of A3 must be decremented before the instruction is executed. The process is known as pre-decrementing.
ARM Example: LDR R0, [R1, #4]!
Similarly, (A3)+ indicates that A3 should be incremented automatically after the instruction has been executed. This process is called post-incrementing.
ARM Example: LDR R0, [R1], #4
In each case the amount of the address increment or decrement is the length in bytes of the indexed operands.

## Slide 24: Register Direct Addressing
In register direct addressing, the name R of the register containing the desired value V(R) appears in the instruction.
Example of the Motorola 680X0 instruction:
MOVE #99, D1
It means “move the constant 99 to data register D1”. It uses immediate addressing for 99 and register direct addressing for D1.

## Slide 25: Register Indirect Addressing
Register indirect addressing refers to indirect addressing with a register R name in the address field.
Example:
MOVE.B (A0), D1
It uses parentheses to indicate that (A0) is an indirect address involving the 680X0’s A0 address register.
This move-byte instruction - the opcode’s .B suffix specifies a 1-byte operand – corresponds to
D1[7:0] := M(A0) and copies the byte addressed by A0 into the low-order byte position of data register D1. The other three bytes of D1 are unchanged.

## Slide 26: Register Indirect with Offset
It is an extension of the register indirect addressing mode.
It can also be viewed as a type of base or indexed addressing.
Example:
SW Rt, OFFSET(Rs)
corresponds to M(Rs+OFFSET) := Rt,
where Rs is the base register and OFFSET is a number acting as an offset operand. Rt is also a register.